        Magic Layout Tool:

1. To select whole layout, click “S”.
2. To place the layout at the centre of the window, press “V”.
3. To see a particular portion in a zoom view, press S to select a particular portion and then press Z, to zoom on that particular portion
4. Now, if we want to know about the particular layer in the layout, follow the below steps:
• Select the particular portion or layer about which you want to know.
• Then, in the tkcon window, run the command “what”
• Then, you will get description about that particular layer in the tkcon window
5. Thus, the first step in magic layout tool is to create a bounding box with a width of 1.38 (3 x
    width(unithd)) and height of 2.72. This can be done by using command
     property FIXED_BBOX {0 0 138 272} in magic tkcon window
6. The syntax to define a bounding box property is:
property FIXED_BBOX {x1 y1 x2 y2}
x1: X-coordinate of the lower-left corner.
y1: Y-coordinate of the lower-left corner.
x2: X-coordinate of the upper-right corner.
y2: Y-coordinate of the upper-right corner.

Bounding Box: A bounding box is a rectangular region that encompasses a set of objects or points in a two-dimensional (2D) or three-dimensional (3D) space. It is defined by the minimum and maximum coordinates of the points it contains. In the context of electronic design automation (EDA) and layout design, particularly in tools like Magic, a bounding box is used to specify the spatial limits of a design or layout cell.
Key Characteristics:
1. Coordinates:
   - Defined by two corners:
     - Lower Left Corner (LLX, LLY): The coordinates of the bottom-left corner of the rectangle.
     - Upper Right Corner (URX, URY): The coordinates of the top-right corner of the rectangle.
2. Dimensions:
   - Width: The horizontal extent of the bounding box, calculated as {URX} - {LLX}.
   - Height: The vertical extent of the bounding box, calculated as {URY} – {LLY}.
   - Area: The total area covered by the bounding box, calculated as {Width}X{Height}.