# Matrix Multiplication Accelerator
## Introduction
A Matrix Multiplication Accelerator is a hardware module designed to perform matrix multiplications efficiently. This operation is fundamental in various fields, such as image processing, machine learning, signal processing, and numerical simulations. By implementing matrix multiplication in hardware, the accelerator can achieve higher performance, lower latency, and reduced power consumption compared to software implementations on general-purpose processors.
## Purpose and Applications
### Purpose:
- Accelerates the computation of matrix products by leveraging parallelism and optimized hardware logic.
- Reduces the computational burden on CPUs or GPUs for specific applications.
### Applications:
- AI/ML: Neural network operations (dot products, tensor multiplications).
- Graphics: Transformations in 3D modeling and rendering.
- Signal Processing: Filtering, convolutions, and other DSP tasks.
## Design Overview
The accelerator is designed to compute the product of two matrices A and B, resulting in matrix C. For a \( N imes N \) matrix multiplication:
        C[i][j] = ∑ (k=1 to N) A[i][k] * B[k][j]

### Inputs:
Two \( N imes N \) matrices (A and B).
### Outputs:
Resultant \( N imes N \) matrix (C).
### Key Features:
- Parallel Computation: Multiple multipliers and adders work simultaneously to perform dot products.
- Pipelining: Improves throughput by overlapping computations.
### Resource Optimization:
Uses time-sharing or resource reuse to fit within the logic gate limit.
## Hardware Implementation
### Constraints:
- Maximum \( N = 2 \) for a \( 2 imes 2 \) matrix multiplier (to meet the Silicluster specifications: 16 inputs, 16 outputs, 1300 gates).
- Inputs/outputs are fed in parallel or serially to meet the input/output limitations.
### Modules:
- Multiplier Block: Performs element-wise multiplication.
- Adder Block: Accumulates products for dot products.
- Control Logic: Synchronizes data flow between multipliers and adders.
### Architecture:
Fully combinational or pipelined design, depending on resource constraints and performance goals.
## Testing and Validation
### Example Test:
Provide fixed test inputs for matrices A and B, such as:
        A = [[1, 2], [3, 4]]
        B = [[5, 6], [7, 8]]

Result:
        C = [[19, 22], [43, 50]]

### Simulation:
Simulate using Verilog testbenches to validate correctness.
## Next Steps
1. Design individual modules for multiplication, addition, and control logic.
2. Integrate these modules into the top-level matrix multiplier module.
3. Simulate and optimize for logic gate constraints.
4. Write a clear testbench for verification.